## Slide 1: Corporate Presentation
June 2018

## Slide 2: Current SiC Application Areas
Server & Datacenter
Electronic Vehicles
Battery Charging
Renewable Energy & Storage
Lighting & Electronic Ballast
Lab & Din Rail PSU

## Slide 3: SiC is at a Tipping Point . . . Electric Vehicle Adoption is a major driver
EV Battery Ad from 1911

## Slide 4: Global EV Sales By Country
EV History and promise
In 2017, China sold 578,000 electric passenger vehicles – 4X that of the US

## Slide 5: UnitedSiC Electric Vehicle Activity
Note: Adapted from TI
Areas of UnitedSiC
Shipments

## Slide 6: UJC Series Ease of Use
Replace IGBTs, SiC MOSFETs or Si Superjunction devices with no change to gate drive voltages

## Slide 7: UnitedSiC FETs Compared to SiC MOSFETs
Normally Off
USCi Cascode
Die Size | (Smaller) RDSA~ 1.75mW-cm2 | (Larger) RDSA~ 3.1- 4.5 mW-cm2
Gate Drive | (Standard) VGS = 0V to 12V OR (SIC) VGS = -10V to 20V | VGS = -5V to 20V
Threshold | VGS(TH) = 5V Typical | VGS(TH) = 2.2V Typical
Intrinsic Diode | Low Qrr, +10% Over Temperature | High Qrr, High VF 3X Over Temperature
Avalanche | Yes | Yes
Short Circuit | Yes | Low
Integrated LV
Si-MOSFET
Additional Antiparallel SiC Diode
Normally Off
Typical SiC MOSFET

## Slide 8: SiC Cascode Gate Drive Benefit
Easy Drop-in
  12V turn-on makes SiC cascode an easy choice for drop-in replacement.
Extra Margin in VGS
  SiC cascode has higher margin in VGS design and requires no negative VGS for turn-off.
Notes: Maximum VGS rating vs. recommended VGS.
SiC MOSFET can be operated at Vgs=0V in some circuits
20
V
-
20
V
0
V
19
V
-
8
V
SiC Cascode
12
V
/
0
V
SiC MOSFET
15
V
/
-
4
V
SiC MOSFET
18
V
/
0
V
22
V
-
6
V
Si IGBT
15
V
/
0
V
25
V
-25
V

## Slide 9: Discrete Packages for SiC
Diodes
Transistors
Largely similar to Si offerings, making them easier to incorporate
Source Kelvin packages
TO247-4L, D2PAK-7L reduces gate ringing, allows faster di/dt operation
Lower inductance DFN8X8 <1.5nH suitable for 650V

## Slide 10: 4 inch SiC JBS Diode Portfolio
Family | Base PN | Description | Samples | RTM | Die | T0-220 | TO-247 | SOT227
650V JBS | UJD06504Z/TS | 650V/4A JBS | Available | Available | MP | MP |  | 
650V JBS | UJD06506Z/TS | 650V/6A JBS | Available | Available | MP | MP |  | 
650V JBS | UJD06508Z/TS | 650V/8A JBS | Available | Available | MP | MP |  | 
650V JBS | UJD06510Z/TS | 650V/10A JBS | Available | Available | MP | MP |  | 
650V JBS | UJD06516K | 650V/16A JBS | Available | Available |  |  | MP | 
650V JBS | UJD06520K | 650V/20A JBS | Available | Available |  |  | MP | 
650V JBS | UJD06550Z | 650V/50A JBS | Available | NA | ES |  |  | 
650V JBS | UJD065100Z | 650V/100A JBS | Available | NA | ES |  |  | 
1200V JBS | UJ2D1205T | 1200V/5A JBS G2 | Available | Available | MP | MP |  | 
1200V JBS | UJ2D1210T | 1200V/10A JBS G2 | Available | Available | MP | MP |  | 
1200V JBS | UJ2D1215T | 1200V/15A JBS G2 | Available | Available | MP | MP |  | 
1200V JBS | UJ2D1220K | 1200V/20A JBS G2 | Available | Available |  |  | MP | 
1200V JBS | UJ2D1230K | 1200V/30A JBS G2 | Available | Available |  |  | MP | 
1200V JBS | UJ2D1250Z | 1200V/50A JBS G2 | Available | Available | ES |  | NA | NA
MP: Mass Production ES: Engineering samples available D: in Development

## Slide 11: 6 inch 650V G3 SiC Diodes
Family | Part number | Description | Samples | Production | Die | Package
650V | UJ3D065200 | 200A 650V JBS diode Die | Available | 2H 2018 | 200A | Wafer
650V | UJ3D065200S | 200A 650V JBS Diode SOT227 | 1H 2018 | 2H 2018 | 200A | SOT227
650V | UJ3D06530TS | 30A 650V JBS diode | Available | MP | MP | TO220-2L
650V | UJ3D06560KS | 2X 30A 650V JBS diode | Available | MP | 30A dual | TO247-3L
650V | UJ3D06516TS | 16A 650V JBS Diode | Available | MP | NA | TO220-2L
650V | UJ3D06512TS | 12A 650V JBS Diode | Q2 18 | Q2 18 | NA | TO220-2L
650V | UJ3D06520TS | 20A 650V JBS Diode | Available | MP | NA | TO220-2L
650V | UJ3D06520KSD | 10A 650V JBS Diode, Common cathode dual | Available | MP | 10A dual | TO247-3L
650V | UJ3D06510 | 10A 650V JBS Diode | Available | MP | 10A | Wafer
650V | UJ3D06510TS | 10A 650V JBS Diode | Available | MP | 10A | TO220-2L
650V | UJ3D06508 | 8A 650V JBS Diode | Available | MP | 8A | Wafer
650V | UJ3D06508TS | 8A 650V JBS Diode | Available | MP | 8A | TO220-2L
650V | UJ3D06506 | 6A 650V JBS Diode | Q2 18 | Q2 18 | 6A | Wafer
650V | UJ3D06506TS | 6A 650V JBS Diode | Q2 18 | Q218 | 6A | TO220-2L
650V | UJ3D06504 | 4A 650V JBS Diode | Available | MP | 4A | Wafer
650V | UJ3D06504TS | 4A 650V JBS Diode | Available | MP | 4A | TO220-2L

## Slide 12: 6 inch 1200V G3 SiC Diodes
Family | PN | Description | Samples | Production | Die | Package
1200V | UJ3D12100 | 100A 1200V JBS diode | Available | Q4 2018 | 100A | 
1200V | UJ3D12100S | 100A 1200V JBS diode | Q2 2018 | Q4 2018 | 100A | SOT227
1200V | UJ3D1250 | 50A 1200V JBS diode | Available | Now | 50A | 
1200V | UJ3D1250K | 50A 1200V JBS diode | Available | Now | 50A | TO247-3L
1200V | UJ3D12100SD | 2X 50 1200V JBS diode Dual | Q2 2018 | Q4 2018 | 50A | SOT227
1200V | UJ3D1220KSD | 2X 10A 1200V JBS diode common cathode dual | Available | Now | 10A | TO247-3L
1200V | UJ3D1210KSD | 2X 5A 1200V JBS diode common cathode dual | Available | Now | 5A | TO247-3L
1200V | UJ3D1210 | 10A 1200V JBS diode | Available | Now | 10A | ES
1200V | UJ3D1210TS | 10A 1200V JBS diode | Available | Now | 10A | TO220-2L
1200V | UJ3D1205 | 5A 1200V JBS diode | Available | Now | 5A | 
1200V | UJ3D1205TS | 5A 1200V JBS diode | Available | Now | 5A | TO220-2L
1200V | UJ3D1202 | 2A 1200V JBS diode | Available | Now | 2A | ES
1200V | UJ3D1202TS | 2A 1200V JBS diode | Available | Now | 2A | TO220-2L

## Slide 13: SiC Diode Differentiator: QC
Best-in-class performance
USCi matched with industry leading die sizes (cost)
Leading the way to foundry based 6inch transition – AEC-Q101 Qualified

## Slide 14: 4 inch 2nd Generation UnitedSiC FETs
Family | Base PN | Description | Samples | Production | Die | TO247-3L
1200V Cascode | UJC1206K | 1200V 60mΩ SiC Cascode | Available | RTM | NA | MP
1200V Cascode | UJC1210K | 1200V 100mΩ SiC Cascode | Available | RTM | NA | MP
650V Cascode | UJC06505K | 650V 45mΩ SiC Cascode | Available | RTM | NA | MP
MP: Mass Production ES: Engineering samples available D: in Development

## Slide 15: 6 inch 3rd Generation SiC JFETs
Family | Part Number | Description | Samples | Production | Die | package
1700V JFET | UJ3N170006 | 1700V 5.6mΩ SiC JFET N-on | Now | TBD |  | Die for SuperCas
1700V JFET | UJ3N170600 | 1700V 600mΩ SiC JFET N-on | Done |  |  | Current limiter
1700V JFET | UJ3N170580 | 1700V 580mΩ SiC JFET N-on | Q2 18 | Q3 18 |  | Die
1700V JFET | UJ3N170580K3S | 1700V 580mΩ SiC JFET N-on | Q2 18 | Q3 18 |  | TO247-3L
1700V JFET | UJ3N170580B7 | 1700V 580mΩ SiC JFET N-on | Q2 18 | Q3 18 |  | D2PAK-7L
1700V JFET | UJ3N1701K6 | 1700V 1.6Ω SiC JFET N-on | Now | TBD |  | Die
1200V JFET | UJ3N120008 | 1200V 7.5mΩ SiC JFET N-on | Q2 18 | Q3 18 |  | Die/ SOT227
1200V JFET | UJ3N120035K3S | 1200V 35mΩ SiC JFET N-on | Q1 18 | Q2 18 |  | TO247-3L
1200V JFET | UJ3N120070K3S | 1200V 70mΩ SiC JFET N-on | Q1 18 | Q2 18 |  | TO247-3L
1200V JFET | UJ3N120140K3S | 1200V 140mΩ SiC JFET N-on | Q2 18 | Q2 18 |  | TO247-3L
650V JFET | UJ3N065005 | 650V 5.3mΩ SiC JFET N-on | Q2 18 | Q3 18 |  | Die, SOT227
650V JFET | UJ3N065025K3S | 650V 25mΩ SiC JFET N-on | Q1 18 | Q2 18 |  | TO247-3L
650V JFET | UJ3N065070K3S | 650V 70mΩ SiC JFET N-on | Q1 18 | Q2 18 |  | TO247-3L
650V JFET | UJ3N065035K3S | 650V 35mΩ SiC JFET N-on | Q2 18 | Q2 18 |  | TO247-3L

## Slide 16: 6 inch 3rd Generation SiC FETs
Family | PN | Description | Samples | Production | Die | Package
1200V Cascode | UJ3C120150K3S | 1200V 150mΩ SiC Cascode | 18-Mar | Q2 18 |  | TO247-3L
1200V Cascode | UJ3C120080K3S | 1200V 80mΩ SiC Cascode | Now | Q1 18 |  | TO247-3L
1200V Cascode | UJ3C120040K3S | 1200V 40mΩ SiC Cascode | Now | Q1 18 |  | TO247-3L
650V Cascode | UJ3C065080K3S | 650V 80mΩ SiC Cascode | Now | Q1 18 |  | TO247-3L
650V Cascode | UJ3C065030K3S | 650V 30mΩ SiC Cascode | Now | Q1 18 |  | TO247-3L
650V Cascode | UJ3C065080T3S | 650V 80mΩ SiC Cascode | Now | Q1 18 |  | TO220-3L
650V Cascode | UJ3C065030T3S | 650V 30mΩ SiC Cascode | Now | Q1 18 |  | TO220-3L
650V Cascode | UJ3C065080B3S | 650V 80mΩ SiC Cascode | Now | Q1 18 |  | D2PAK-3L
650V Cascode | UJ3C065030B3S | 650V 30mΩ SiC Cascode | Now | Q1 18 |  | D2PAK-3L
650V Cascode | UJ3CF065040K3S | 650V 40mΩ SiC Cascode Fast | Mar-18 | Q2 18 |  | TO247-3L
650V Cascode | UJ3CF065040T3S | 650V 40mΩ SiC Cascode Fast | Mar-18 | Q2 18 |  | TO220-3L
650V Cascode | UJ3CF065040K4S | 650V 40mΩ SiC Cascode Fast | Mar-18 | Q2 18 |  | TO247-4L
650V Cascode | UJ3CF065030K4S | 650V 30mΩ SiC Cascode Fast | Jan-18 | Q2 18 |  | TO247-4L
650V Cascode | UJ3CF065080K4S | 650V 80mΩ SiC Cascode Fast | Jan-18 | Q2 18 |  | TO247-4L
1200V Cascode | UJ3CF120150K4S | 1200V 150mΩ SiC Cascode Fast | 18-Apr | Q2 18 |  | TO247-4L
1200V Cascode | UJ3CF120080K4S | 1200V 80mΩ SiC Cascode Fast | 18-Jan | Q2 18 |  | TO247-4L
1200V Cascode | UJ3CF120040K4S | 1200V 40mΩ SiC Cascode Fast | 18-Jan | Q2 18 |  | TO247-4L
650V Cascode | UJ3SCF065040K4S | 650V Stack 40mΩ SiC Cascode Fast | 2H 2018 | 2H 2018 |  | D2PAK-7L
650V Cascode | UJ3SCF065030K4S | 650V Stack 30mΩ SiC Cascode Fast | 2H 2018 | 2H 2018 |  | D2PAK-7L
650V Cascode | UJ3CF065080K4S | 650V 80mΩ SiC Cascode Fast | 2H 2018 | 2H 2018 |  | D2PAK-7L
1200V Cascode | UJ3CF120150K4S | 1200V 150mΩ SiC Cascode Fast | 2H 2018 | 2H 2018 |  | D2PAK-7L
1200V Cascode | UJ3CF120080K4S | 1200V 80mΩ SiC Cascode Fast | 2H 2018 | 2H 2018 |  | D2PAK-7L
1200V Cascode | UJ3SCF120040K4S | 1200V Stack 40mΩ SiC Cascode Fast | 2H 2018 | 2H 2018 |  | D2PAK-7L
650V Cascode | UJ3SCF065040K4S | 650V Stack 40mΩ SiC Cascode Fast | 2H 2018 | 2H 2018 |  | DFN8X8
650V Cascode | UJ3SCF065030K4S | 650V Stack 30mΩ SiC Cascode Fast | 2H 2018 | 2H 2018 |  | DFN8X8
650V Cascode | UJ3SCF065080K4S | 650V Stack 80mΩ SiC Cascode Fast | 2H 2018 | 2H 2018 |  | DFN8X8

## Slide 17: Gen 3 FETs vs Current Products
TJMAX rating raised to 175 oC
VGSMAX rating raised to +/- 25V
Built-in ESD protection diodes between MOSFET gate-source
Compatible with all forms of standard Si and SiC gate drive voltages, with plenty of positive and negative voltage margin
Current rating increased by reducing RTHJC (same die size, improved die attach technology)
Rdson at 150 oC improved compared to G2
No change to UIS rating, able to handle high peak currents in avalanche
Switching losses decrease with Tj, due to the reduction of JFET Rg with temperature
Similar switching speed in turn-on/turn-off using SiC JBS freewheeling diode

## Slide 18: Cascode Operation

## Slide 19: 650V – FET Technologies Compared
Silicon Superjunction
Vertical current flow
GaN HEMT
Lateral current flow
SiC
Vertical current flow
Trench MOS
Trench JFET
substrate
substrate
substrate
substrate
Drain
Drain
Drain
Drain
Source
Source
Source
Source
P-col
N-col

## Slide 20: 650V FET Comparisons
PFSB Efficiency Vin=400V, Vo=48V, 75kHz

## Slide 21: 100A, 1200V SiC Cascode Stack Advantage
8mohm, 1200V switch in just 5.5X6.5mm (100A, 1200V)
All the advantages of cascodes
Simplifies module packaging, no antiparallel diodes
Building block for high current modules of all types
  HB, FB, 3-PHASE, TNPC, NPC
  Promising for EV applications
As the world moves to multilevel architectures, the inside of the module will become even more complex.
UnitedSiC’s Cascode Stack enables simplification through fewer components, creating more space within the highly complex architecture and ultimately displacing the diode.
SiC MOSFET + JBS 1200V
100A X 3
100A Stack 1200V
100A X 3

## Slide 22: Supercascode: The next generation of devices > 3.3kV
Configuration 1: Traditional
Configuration 2: Supercascode
5 parallel 250 mΩ, 6500 V device N-off
5 series 10 mΩ, 1200 V devices
Develop and use devices with high voltage rating
High device voltage rating requires thick epi layer
Thick epi increases RDSA, requiring multiple parallel devices for acceptable efficiency
Thick epi increases device cost, switch development cost and development risk
Use commercial devices with 1.2-1.7kV rating in series and a Si MOSFET for control
Low device voltage rating enables use of commercially available devices
Low component / module cost
Low development risk and short development time
Patented design constructed from Normally On JFETs, providing breakthrough cost and performance

## Slide 23: Supercascode Performance
Very low Ciss and Crss
Lower Coss than standard modules
Low Gate Drive Requirements
Extremely Low Reverse Recovery Charge
N-off JFET Half-bridge vs. Supercascode
Datasheet Comparison
Extremely low reverse recovery charge (basically capacitive charge like SiC JBS diode)
Comparisons of the proposed power module, 6.5kV–100mW SiC normally-off JFET module and 6.5kV-85A Si IGBT module
N-off JFET half-bridge module
Supercascode module

## Slide 24: UnitedSiC 650V SiC FETs Surpass Super-Junction
Test results of cascode drop-in replacement of super-junction MOSFET in phase shift full bridge
Phase shift full bridge (PSFB) circuit with synchronous rectifier (SR) output
UJC06505K
MOSFET SRs
Greatly reduced capacitances = faster switching
Vgs
Vds

## Slide 25: Cascode Enables High Voltage PSFB
Combination of low RDS(on), 1200 V rating, and extremely low capacitances
With high output voltage, a full-bridge Schottky diode rectifier yields lowest loss
Small, 1200 V Schottky clamp diodes arrest ringing new part UJ3D1202D
Typical application: on or off-board electric vehicle charger
700 to 800 V input
USCi 1200 V Cascode:
UJ3C1202KS
UJC1206K
UJC1210T/K
UJC1220T/K
USCi 1200 V Schottky Diode:
UJ2D1220K
UJ2D1230K
USCi 1200 V Schottky Diode:
UJ3D1202D
UJ2D1205T

## Slide 26: 650V cascode – Totem Pole PFC
Chart: Output Power (W)
| 199.486118 | 278.54007899999999 | 357.4904159999997 | 436.24403100000001 | 514.55048699999998 | 593.43914599999971 | 672.08852000000002 | 751.03547800000001 | 829.77241300000003 | 908.15573300000005 | 987.42977699999994
UJC06505 at 115 VAC | 0.94987 | 0.96512 | 0.97298 | 0.97773 | 0.98055 | 0.98231 | 0.98277 | 0.98361 | 0.98352 | 0.98219 | 0.98259
UJC06505 at 230 VAC | 0.97886 | 0.98295 | 0.98655 | 0.98886 | 0.9903 | 0.99143 | 0.99242 | 0.99305 | 0.99357 | 0.99384 | 0.99399
Uniquely qualified for use in CCM Totem Pole PFC due to excellent Body Diode

## Slide 27: Solar Inverter Applications
As with an AFE, compact and efficient solar inverters are made possible by low RDS(on) with high voltage rating combined with excellent reverse conduction and recovery characteristic
Low reverse conduction loss eliminates need for bypass diodes, even at high switching frequency
Extremely high efficiency is possible due to very low switching loss
Three-level is “standard” for new solar designs
  Enables high input voltages, up to 1700 V
  Can use switching algorithm with either NPC or TNPC topology to reduce or eliminate common-mode voltages
Three-level TNPC inverter
Three-level NPC inverter
USCi 1200V Cascode:
UJ3C120150K3S
UJ3C120080K3S
UJ3C120040K3S
UJ3C120150K4S
UJ3C120080K4S
UJ3C120040K4S
USCi 650V Cascode:
UJ3C065030K3S, UJ3C065030K4S
UJ3C065080K3S, UJ3C065080K4S
USCi 650 or 1200V Diode:
UJ3D06520KSD or U32D1220KSD
UJ3D06530TS or U32D1210KS

## Slide 28: TNPC Power blocks with Cascodes 4-cell parallel

## Slide 29: Ultra Low RDS Devices – Power Routing
1.7mohm, 1200V switch in SOT227 footprint
>2X smaller than any SiC MOS alternative
Parallels 6X 8.1mohm Stack cascodes
In development
Ultra-small/Ultra-light low resistance high voltage switches
Solid state breakers and power controllers
2X lower Rds than MOSFETs in a given footprint
20mm
25mm
G
D
S
S

## Slide 30: Summary
SiC Diodes
Best-in-class performance
Highest currents available
UnitedSiC unmatched with industry leading die sizes
SiC JFET
Best in class devices for specialized protection applications
SiC FETs
Ease of use (Universal 12V/0V or 20V / -5V Gate Drive)
Performance (Low Vf , Qrr Body-diode, switching energies)
Reliability (No SiC Gate oxide, No SiC body diode, 5V Threshold voltage)
No SiC FWD necessary
Technical Support
App Notes, Datasheets and SPICE models available at www.unitedsic.com
Various Eval Boards already available (PSFB, Totem Pole PFC, Flyback, H-Bridge)
Contacts:
  J. Christopher Dries – President and CEO – jcdries@unitedsic.com – 732-355-0550